## Slide 1: Proton interrogation of passenger and cargo vehicles at near-background dose levels to identify shielded nuclear threats
Seth Van Liew
Passport Systems, Inc.
North Billerica, MA
5/24/17

## Slide 2: Outline
Cargo scanning technologies
Low-dose protons
Material ID with protons
Nuclear detection
Proton sources
Conclusions and next steps

## Slide 3: Motivation
A solicitation a few years back called for detection of nuclear materials at human safe radiation levels
A senior scientist at the company said it was “impossible”
I wasn’t so sure, and suggested protons
  Low dose if Bragg peak is outside of the human body
  Accurate imaging possible at low doses from monitoring the range
  Proton current can be adjusted to make scanning as fast as possible
Straightforward to get grayscale images based on range of protons in the detector
  Analog for areal density
  Not a perfect relationship as stopping power is material-dependent
  But can we use that?

## Slide 4: Cargo screening at ports and borders
Mandated 100% screening
  It’s more like a few percent in practice
Dangerous materials: explosives, nuclear materials, guns
Contraband: drugs, cigarettes, people, other cargo
Most scanners use x-ray technology
Most identification of threats done by operators using “context”
Desire a “red light green light” system
Want to minimize secondary scans
Identification of threats can be done automatically using atomic number, density, neutron energy, nuclear / x-ray fluorescence, shape

## Slide 5: Cargo scanning technology
X-rays
Sniffers
Muons
Protons

## Slide 6
 | X-rays | Sniffers | Muons | Protons
Radiograph | X |  | X** | X
Material discrimination | X | X | X | X
Nuclear detection | X* |  | X | X
Fast scanning | X | X |  | X
Low dose |  | X | X | X
Cheap | X* | X | ?? | 
* Cannot achieve nuclear detection and have a cheap x-ray cargo system
** Muons can only create a realistic radiograph after a LONG time

## Slide 7: Why are protons lower dose?
X-rays are stochastic, depositing dose in a statistical distribution that is a decaying exponential
Protons are deterministic and have a well-defined range
60% of proton dose occurs in the last meter of travel (for this system)
This Bragg peak becomes sharper with heavier ions

## Slide 8: Initial system parameters
Wanted to mimic a cargo x-ray system for comparison
Most x-ray systems have steel penetration of between 300 and 400 mm
At 800 MeV, protons have a range of about 420 mm in steel
  At 500 MeV, range in steel is 210 mm
Maximum proton current in the hundreds of pA
For human scanning, a 20 m long cargo container at 60 kph will be scanned in 1.2 s with a proton current of 0.89 pA and dose of 0.23 µSv
Detector concept still uncertain
  Used water at an early stage to establish baseline
Standard cargo truck is a little over 3 m high, so chose a 4 m high detector
Chose parallel beam of protons so image wouldn’t be distorted
  This can be accomplished with bending magnets

## Slide 10: Grayscale image with protons

## Slide 11: To raster or not to raster
Rastering refers to having a set distance between protons and a sequential scanning pattern
Rastering creates image artifacts
It limits spatial resolution
It restricts proton current if linear raster used
Random distribution far better
  Arbitrarily high resolution
  Higher proton current
  Fewer image artifacts

## Slide 12: Detector concept
Need to reliably find range
Want to establish position and angle of protons entering and exiting the cargo
  This turned from a nice-to-have to a necessary requirement
Due to environment dose considerations, did not want protons scattering out of the detector or passing beyond the end

## Slide 13: Detector hardware
MWPC’s
  Similar to Geiger counter, use ionization of gas as proton passes through
  Can read out position information
  Cheap (or rather, “cheap”)
  Gas handling system, high voltage required
Aluminum drift tubes
  Similar to MWPCs
  Minimize proton interactions with detector
  No way to reliably establish range
Silicon
  Excellent spatial resolution
  No gas handling or vacuum
  No high voltage
  Way too expensive
Plastic scintillator
  Heavy but cheap
  Strongly deflects protons but also stops ‘em
  No gas handling or vacuum
  No high voltage

## Slide 14: Plastic scintillator detector
Protons create visible light in PVT
This light can be read out directly via PMT
It can also be transmitted via wavelength-shifting fiber embedded within the scintillant
Read out using SiPMs
  Biased to about 70 V
Each tile 50 cm wide x 200 cm tall x 10 mm deep
  Can limit range resolution
Each tile coated with optical reflector
Entire detector a few hundred thousand in material costs
Segmentation maximizes proton current and keeps tile size manageable

## Slide 15: Is there a way to make the detectors more compact?
Can interleave scintillant with steel
Lose some spatial resolution
Can make a detector less than 1 m deep and narrower
steel
PVT

## Slide 16: Material identification with protons
Proton attenuation through matter is dependent on Z and A
Although we don’t know a priori how much material the proton passes through, this relationship governs the statistical distribution of the final range
Higher atomic number materials have a larger standard deviation in the final range
This effect is called range straggling

## Slide 17: LANL proton material ID
Reconstructs different image planes
Does not need proton range to generate image and establish material ID
Minimal interaction of proton with detector
Excellent contrast and separation of MCS and nuclear scattering
Uses bending magnets on detector side
Limited field of view

## Slide 18: LANSCE pRad concept

## Slide 19: Material ID through range straggling
Irradiated 10 cm x 10 cm squares of different materials and different thicknesses
Can easily distinguish different materials based on range straggling alone
Not great for thin materials
Requires a full distribution of protons
Can we do material ID with a single proton to keep the dose low?

## Slide 20: Material identification with single protons
Electron scattering proportional to Z/A from Bethe-Bloch equation
Moliere scattering governs nuclear scattering events, which can be large angle
Unfortunately, there are many variables that govern scattering angle in addition to material
  Atomic screening
  Interaction length
In addition, accurate track reconstruction is necessary to establish the point of interaction and thus the scattering angle
Proton can interact much more in a detector than in the actual target, complicating matters further

## Slide 21: Different approach: just look at distribution
In x-ray inspection systems, wedges of different materials are scanned to establish relationship between signal levels and materials
The plotted results are calibration curves and can be used to fit unknown materials
Would this approach work for protons?

## Slide 22: Material ID through lateral straggling
A proton’s lateral deflection is more deterministic
Can reliably get material ID with few protons
Good for both thin and thick materials
Good material separation at all atomic number values

## Slide 23: System properties
Pixel sorting
  Done by incident proton position only
Proton current - pA
Variable resolution
  Can be set differently within same scan
Secondary inspection of region of interest at higher dose
Auto segmentation to establish material ID
  We use all protons for an entire object
PINTO (Proton Imaging and Nuclear Threat Optimization) algorithm
  Determines material ID through lateral deflection
  Determines material density through large angle scattering

## Slide 24: Material ID results
Based on 10 cm x 10 cm squares of material
Dose is 2 µSv

## Slide 25: Different materials, different attenuations
HDPE
Iron
Tin
Lead
0.1
0.4
0.7
0.9
0.1
0.4
0.7
0.9
Range
fraction

## Slide 26: Different doses
HDPE
Iron
Tin
Lead
0.1
0.4
0.7
0.9
0.1
0.4
0.7
0.9
Range
fraction
0.2 µSv
2 µSv

## Slide 27: Imaging cluttered cargo

## Slide 28: Nuclear detection
The difference between uranium and lead is only about 10% in Z
Although the system can distinguish this, it’s not definitive
There is, however, a big difference in density
Fissile materials (U, Pu, Th) are both high Z and high density
Considered nuclear material “identified” if I could reliably establish Z and density
For experiments, I used 15 cm cubes of uranium shielded by 2.5 cm of lead
  Above critical mass of U 235?

## Slide 29: Density determination
Incoming and exiting angle determined by detectors
Large angle measured and averaged over a given threshold
Ratio of large angle deflections to total number of protons calculated
Density determined based on this ratio
Probable interaction point established to enable 2D localization
  Similar to POCA
  Rudimentary 3D localization also possible

## Slide 30: Can we distinguish lead from uranium?
There is enough contrast in grayscale to see that something is different
  (Each image is normalized)
Image dose is 1.2 µSv
However need material ID
Contrast is visible at low doses
Lead only
Lead shielded uranium
0.2 µSv

## Slide 31: Can we distinguish lead from uranium?
With the material discrimination from PINTO, we can see further contrast, but still not much
Lead and Uranium are only 10% different in atomic number or so, 82 vs. 92.
Lead only
Lead shielded uranium

## Slide 32: Adding in density enhancement
By applying the density difference to the color scheme, a marked difference in material properties can be seen
This difference is still seen even at low doses in the bottom image
0.2 µSv
1.2 µSv

## Slide 33: Proton sources – is that all we need?
Accelerating protons is not a cheap business
Linear accelerator
  Quite long for 800 MeV protons
  High extraction yield
  Straightforward technology
Cyclotron
  Well-established technology
  More compact, but still large
  Low extraction efficiency
Sychrotron, synchro-cyclotron
  Require super-conducting magnets and sophisticated electronics
  Compact
  Expensive

## Slide 34: 590 MeV cyclotron, PSI, Switzerland

## Slide 35: Emerging proton technologies
Dielectric wall accelerator
  Similar to linac: uses travelling wave to induce acceleration
  Main difference with linac is it uses high-gradient insulators
  Can achieve 100 MV/m accelerations
Laser / plasma accelerated protons
  Uses wakefield or induced electric field to accelerate charged particles
  Highest yield current come from shining a laser through a gas
  Still not achieving high energies, but rapidly improving
Both technologies offer potentially cheap and compact way to generate protons

## Slide 36: Can we use a lower proton energy?
Short answer: yes!
Longer answer: eh…
Material ID still good at lower energies
Penetration goes down rapidly with decreasing energy
  Only 220 mm steel penetration at 500 MeV
500 MeV calibration

## Slide 37: What’s next?
Experimental validation and prototype
Low-dose 3D techniques
  The built-in density determination has 3D already encoded
Other applications:
  Medical
  Space
  Specialized

## Slide 38: Conclusions
Protons offer superior scan speed and detection while giving low dose
Large-scale radiography of vehicles with compact detector designs possible
Material identification at the full range of densities and atomic numbers demonstrated
Shielded special nuclear materials can be identified at doses of 0.2 µSv, suitable for members of the public
Protons are still expensive to generate, but emerging technologies may change that
3D imaging possible
Other opportunities for this technology outside of security

## Slide 39: Thank you!

## Slide 40: Plasma acceleration

## Slide 41: Proton plasma acceleration