## Slide 1: Polarized Solid Targets for Hadron Beams - Overview
Choosing a target for Drell Yan Experiments

## Slide 2: Issues
Type of Refrigerator and Recent Experiments
Polarizable Materials
Beam Heating and Radiation Damage
Adiabatic Fast Passage (FP)

## Slide 3: Choosing a Refrigerator and “Recent” Experiments
High Intensity > 109 to < 1012 particles/sec
Use 4He Evaporation Refrigerator and ~ 5 T Magnet
Low Intensity < 109 Particles/sec
Dilution Refrigerator 3He/ 4He mixture
Very Low Intensity <107 Paricles/sec
Frozen Spin Refrigerator
Chris Keith’s Talk

## Slide 7: “Recent” Experiments (Since ~ 1990)
SLAC (E143,E155,E155X)
Electrons ~ 9 -50 GeV Duty Factor 10-4
Average Intensity ~ 100nA (~ 6 1011 e/sec)
BNL (AGS)
Protons 24 GeV, Duty Factor ~30%
Average Intensity ~ 10 11 protons/sec
JLab (6 experiments, two 4He fridges)
Electrons 1 -6 GeV Duty Factor 100%
Average current ~100nA and ~ 5nA

## Slide 8: Related Experiments
CERN (EMC, SMC, COMPASS)
muon beams, 100 - 200 GeV
Jlab (FROST)
photon beams 1 – 3 GeV

## Slide 9: Target Materials
Properties: High absolute Polarization and
dilution factor
Fast build up
Slow Polarization Decay
(radiation damage resistance)
Talk by James Maxwell
Fast Reversal ? AFP?
Talk by Patrick Hautle

## Slide 10: Radiation resistant materials
Ammonia and deuterated ammonia
Proton polarizations > 90%
Deuteron Polarizations ~ 50%
Lithium Hydrides
7 LiH ~50% at 5 T and 1 K
6LiD ~ 30% at 5 T and 1K for both

## Slide 17: Adiabatic Fast Passage (AFP)
Apply RF pulse to target and if certain conditions are met, the ensemble of spins (or a fraction of them) will flip.
Talk by Patrick Hautle