## Slide 1: Internal target option for RHIC Drell-Yan experiment Wolfram Fischer and Dejan Trbojevic
31 October 2010
Santa Fe Polarized Drell-Yan Physics Workshop
★
Notes: 25+10 min total

## Slide 2: Content
Layout of internal target experiment b* considerations, orbit correction
Low density target option– 1015 atoms/cm2 low density = operation in parallel to STAR and PHENIX
High density target option – 1017atoms/cm2 high density = dedicate operation after store for STAR and PHENIX

## Slide 3: Drell-Yan experiment proposal with internal target
Notes: Apparatus from E906 (Fermilab)

## Slide 4: Orbit effects
2 dipoles (11, 3 mrad bend) with same polarity (RHIC arc dipoles bends 38 mrad)
Beams largely shielded (see next slide)
For comparison: RHIC orbit corrector has 0.3 mrad (at locations with larger b-functions)

## Slide 5: Orbit effects
If we drill a R=5 cm through hole, then field drops to 0.336 T
(magnetic length will increased by 10 cm)
By = 0.1662 T
R = 5cm: 1.3 Tm R = 2cm: 0.6 Tm
+ ~20% from 2nd magnet
[RHIC arc dipole corrector: ~0.3 Tm )
Needs further work, likely not a showstopper for small radius.

## Slide 6: b* considerations
Have operated BRAHMS mostly with b* = 3.0 m (until Run-6)
Have also used
  b* = 2.0 m (d-Au at 100 GeV/nucleon, Run-3, lifetime/background problems)
  b* = 2.5 m (Cu29+ at 100 GeV/nucleon, Run-5, lifetime/background problems)
  b* = 3.0 m (Cu29+ at 11.2 GeV/nucleon, Run-5)
  b* = 3.0 m (31.2 GeV p, Run-6)
b* = 2.0 m possible (perhaps even b* = 1.0 m)
[not critical for internal target, see next slide]
May need power supplies for local correctors can be studied with dynamic aperture simulations (Y. Luo)

## Slide 7: b* considerations
So far all consideration were for b* at nominal IP
Internal target is at s = -7.0 m where b should be as small as possible (to both maximize luminosity and minimize emittance growth of proton beam)
With b* at nominal IP:
bmin = 14m at s = -7m (reached for b* = 7 m)
RMS beam size for - bmin = 14m - en = 20 mm.mrad - 250 GeV protons is 1 mm => need ~4 mm target width for full overlap

## Slide 8: Beam lifetime with internal target D. Trbojevic
[D. Trbojevic, “Beam lifetime and emittance growth in RHIC under normal operating conditions, with the hydrogen gas jet, the cluster jet and pellet targets”, BNL C-AD/AP/403 (2010)]
t lifetime
N particle number
t time
n target density
l interaction length (= circumference)
f revolution frequency
sN cross section for nuclear interactions leading to loss
sC cross section for Coulomb interactions leading to loss

## Slide 9: Emittance growth with internal target D. Trbojevic
[D. Trbojevic, “Beam lifetime and emittance growth in RHIC under normal operating conditions, with the hydrogen gas jet, the cluster jet and pellet targets”, BNL C-AD/AP/403 (2010)]
eN normalize emittance
bTWISS twiss function
Q scattering angle
mp target density
c speed of light g Lorentz factor
ZP, AP particle Z and A
c speed of light
LRAD radiation length
a fine structure constant
Nm gas density (molecules/g)
ZT, AT target Z and A
nm gas density (g/cm3)
re classical electron radius
RT Thomas-Fermi screening radius
RN effective radius of target nucleus

## Slide 10: Low density internal target – 1015 atoms/cm2
Low density H target (storage cell, cluster) for continuous operation in parallel to PHENIX and STAR
With 1015 atoms/cm2
  beam lifetime: tN = 15 h initial loss rate of 4x108 p/s + secondary particles
  luminosity lifetime: tN < 7.5 h
  emittance growth: deN/dt ~ 10-2 mm mrad/h
  luminosity loss to PHENIX and STAR (10 h store): ~% range
Need to reduce target density by about factor 3-5 tN ~ 50 h without target under current conditions

## Slide 11: Beam lifetime in Run-8 pp (100 GeV)
Expect proton beam lifetimes at 250 GeV to approach these values in the future.
Intensity fitted to N(t) = A*exp(-t/t1) + (1-A)*exp(-t/t2) [first 3h]
slow part, A = 10%
slow part, 1-A = 90%
50 h

## Slide 12: Luminosity lifetime in Run-8 pp (100 GeV)
Expect proton beam lifetimes at 250 GeV to approach these values in the future.
Luminosity fitted to L(t) = A*exp(-t/t1) + (1-A)*exp(-t/t2) [first 3h]
slow part, A = 12%
slow part, 1-A = 88%
14 h

## Slide 13: High density internal target – 1017 atoms/cm2
High density target (pellet, solid) for end-of-store operation after PHENIX and STAR
With 1017 atoms/cm2
  beam lifetime: tN = 0.15 h initial loss rate of 4x1010 p/s + secondary particles
  emittance growth: deN/dt ~ 1 mm mrad/h can cause beam losses in other parts of ring
  luminosity loss to PHENIX and STAR (10 h store): ~2-3% due to lost time in overall cycle DY experiment becomes the beam dump

## Slide 14: Luminosity loss to STAR and PHENIX for end-of-store operation
operation ok right of line
Assumptions:
12 h from beginning of store to next (without DY experiment)
end-of-store run with length of 1.5x beam lifetime (Nb,final = 0.22 x Nb,initial)

## Slide 15: High density internal target – 1017 atoms/cm2
With high density target beam loss at internal target is similar to beam dump
Internal target will become effectively the beam dump
Will need shielding and radiation control like at dump
In particular need shielding for superconducting magnets in area (especially DX)
Electronics in experimental hall needs to be radiation hard

## Slide 16: Polarized proton intensity upgrades
Bunch intensity
Polarized source upgrade under way 10x intensity, ~5% more polarization (2013) could translate in about 3x1011 p/bunch
new SAD/ASE (under way)
Number of bunches (>111) requires
new SAD/ASE (under way)
new RHIC injection system
likely in-situ coating of beam pipe (R&D under way)
possibly another dump upgrade (just finished one – beam pipe inserts)
improved machine protection system (loss control on ramp, during store)
existing OPPIS
In-situ pipe coating SEY and r reduction (start >2013)

## Slide 17: Other ideas – target surrounding beam (E. Stephenson)
Plan experiment to measure polarization at large amplitudes (M. Bai).

## Slide 18: Summary
Internal target is an option for beam operation
Layout of internal target experiment orbit distortion with shielded fields probably ok bmin = 7.5 m at s = -7 m, need ~4 mm target width for full overlap
Low density target option – 0.3x1015 atoms/cm2 parasitic operation to STAR and PHENIX, (%-range luminosity loss)
High density target option – 3x1016 to 1017atoms/cm2 end-of-store operation, few % luminosity loss to STAR and PHENIX target becomes beam dump
Higher bunch intensity upgrade under way

## Slide 19
Additional material

## Slide 20: b* considerations
Field quality of triples in IR2 not as good as IR6 and IR8
Local IR correctors installed in IR2 (like IR6 and IR8) but have currently no power supplies connected have used full complement in IR6/IR8 in operation: 6-poles, skew 6-poles, 8-poles, 10-poles, 12-poles
Small b* implies large bmax in triplets (b*bmax = const ~ 1.5 km) and therefore larger exposure of beam to triplet field errors
These cause emittance growth and beam lifetime reduction through the enhancement of chaotic particle motion (the reason for all beam loss)

## Slide 21: b* considerations
[F. Pilat et al., “Non-linear effects in the RHIC interaction regions, …”, PAC 2003.]
RHIC interaction region with nonlinear correctors
Full corrector set (like IR6/IR8): 14 ps per beam Reduced set (6-pole, skew 6-pole): 4 ps per beam About $12k per 50A ps (+infrastructure, controls, and installation: ~$100k)